## Slide 1: Mid Circuit Measure & Reset
ECE-592 Quantum Computing
Ashwin Karthik (ashanka7)
Pradeep Vetapalem (vkrish7)

## Slide 2
Introduction
Reuse qubits in same circuit
Reuse qubits and merge jobs
Error Correction

## Slide 3
Reuse:
More wait times with jobs involving more qubits.
Limited number of qubits on the HW.
Less execution time when jobs are merged.
Error Correction.
Why Measure and Reset?

## Slide 4: Application-1:
Reuse qubits in the circuit:
Circuit implemented: n-bit full adder
Number of qubits used: 4(fixed) IN1, IN2, C0, C1
Initial setup | Addition-1 | M&R | Addition-2 | M&R | Addition-3…
= 0 | = 0 | Reset | = Carry[1] | NOP | = Carry[1]
= A[0] | = A[0] | Reset | = A[1] | Reset | = A[2]
= B[0] | = Sum | M & R | = Sum | M & R | = Sum
= 0 | = Carry[0] | NOP | = Carry[0] | Reset | = Carry[2]
Initial setup | Addition-1 | M&R | Addition-2 | M&R | Addition-3…
 |  | Reset |  | NOP | 
 |  |  |  | Reset | 
 |  | NOP |  | Reset | 

## Slide 5
Application-1: ADD(4’b1111,4’b1111)

## Slide 6
Application-1:
Chart: Probability values
| Str_len_1 | Str_len_2 | Str_len_3 | Str_len_4 | Str_len_5 | Str_len_6 | Str_len_7 | Str_len_8
Rst_cnt_1 | 0.656 | 0.528 | 0.339 | 0.288 | 0.175 | 0.14 | 0.086 | 0.072
Rst_cnt_2 | 0.651 | 0.526 | 0.307 | 0.255 | 0.183 | 0.138 | 0.092 | 0.073
Rst_cnt_3 | 0.679 | 0.506 | 0.33 | 0.236 | 0.167 | 0.114 | 0.085 | 0.074
Rst_cnt_4 | 0.667 | 0.508 | 0.295 | 0.259 | 0.165 | 0.143 | 0.088 | 0.072
Rst_cnt_5 | 0.66 | 0.498 | 0.343 | 0.256 | 0.176 | 0.139 | 0.087 | 0.074
We reused all the qubits instead of just ancilla bits. On instantiated multiple qubits for each input, we saw improvement in probabilities, but didn’t observe fidelity increase trend over
Increase in resets count.

## Slide 7
APPLICATION 2: FUSING SIMON AND BERNSTEIN VERZERANI CIRCUIT USING MID CIRCUIT MEASUREMENT AND RESET
A 2 BIT BERNSTEIN VERZERANI CIRCUIT FUSED WITH 2 BIT SIMON CIRCUIT

## Slide 8: Application-2:
The Comparison was made between time taken when circuits run as separate jobs vs run as combined job.
Combining the jobs resulted in significant reduction of total runtime.
The scheme was tested for string lengths
ranging from 1 to 5. The run-time improved
by two folds on an average.
Chart: String Length
BV+SM (Total Combined Execution Time) | 5 | 5.3 | 5.5 | 6.2 | 6.5
BV+SM (Total Seprate Execution Time) | 10.6 | 10.1 | 10.4 | 10.9 | 11.6
Fusing multiple Jobs
EXECUTION TIME ANALYSIS

## Slide 9: Application-2:
Fusing multiple Jobs
FIDELITY ANALYSIS
Chart: String Length
BV+SM | 0.99609 | 0.86619 | 0.173 | 0.04153 | 0.02342
SM | 0.9804 | 0.922 | 0.8669 | 0.4759 | 0.5056
Combining the jobs had better runtime but comes with a trade off.
The fidelity decreases rapidly as the string length increased exhibiting sub-optimal performance than running Simon separately.
Noise caused by resetting and reusing the qubits

## Slide 10
Error Correction:
Application-3:

## Slide 11
M : 0/1
N: Correction bits used
Noise Model: ibmq_mumbai
Correction logic:
1. Simulate the circuit and collect top ‘N’ values.
2. If 1’s >= 0’s , inc. ones_count. Else inc. zeros_count.
3. Run the same for 1->N.
Correction rate: 100% (1-8 correction bits)
Manual tweaking of NoiseModel gave mismatches post correction.
Application-3:

## Slide 12: Future plans:
Improve the full adder circuit to achieve better probability over reset counts.
Improve the BV+Simon fusion circuit to see better fidelity.
Implement more sophisticated Error Correction circuit where a single correction bit can detect and fix errors in multiple qubits.

## Slide 13: Thank you!
Q&A: